## Slide 1
Pump
Sparge Tank or tap connection
Mash Tun
Sensor Assembly
Needle valve
Element
Sensor Assembly
Brew Kettle
Stage 1: Cleaning (optional)
Fill system with water by connecting Input 1 to a household tap
Input 1
Valve 1 will then open allowing x amount of water into the Brew Kettle
Valve 1
Valve 2
Valve 3
Valve 1 will then change inputs and the pump and heater will turn on, pumping hot water throughout the system for a user defined time period
Valves 2 and 3 will also open to allow sanitisation of the mash tun
The waste water is then pumped out of the system and cleaning is complete

## Slide 2
Pump
Sparge Tank or tap connection
Mash Tun
Sensor Assembly
Needle valve
Element
Sensor Assembly
Brew Kettle
Stage 2: Mash
Fill system with brewing water by connecting Input 1 to a household tap or “sparge tank” The user will also be prompted to add their grains to the mash tun at this point.
Input 1
Valve 1 will then open allowing a user defined amount of water into the Brew Kettle.
Make any desired chemical adjustments to the water at this point
Valve 1
Valve 2
Valve 3
Valve 1 will then change inputs and the pump and heater will turn on, pumping hot water throughout the system until the “strike” temperature is reached
Once strike temperature has been reached, valves 2 and 3 will open allowing hot water to pass through the grains in the mash tun. This step will be different if the user is using an internal grain basket or “Brew in a Bag” method.
The hot “wort” is continually recirculated and the user defined temperature maintained until the mash stage is complete.

## Slide 3
Pump
Sparge Tank or tap connection
Mash Tun
Sensor Assembly
Needle valve
Element
Sensor Assembly
Brew Kettle
Stage 3: Sparge
Input 1
Valve 1
Valve 2
Valve 3
The user can chose “no sparge” or to input sparge water directly from a household tap, or from a dedicated sparge tank if chemical adjustments to the sparge water are desired
Valve 1 then opens allowing sparge water to pass through the grain bed in the mash tun.
The sparge water flow rate is automatically adjusted by varying the needle valve to ensure the correct temperature water is delivered to the grain bed.
Once the desired amount of sparge water has been delivered to the mash tun, valve 1 switches inputs and the pump and heater element are turned off. The controller will then wait until all sparge water has been drained from the mash tun before proceeding to the next stage.

## Slide 4
Pump
Sparge Tank or tap connection
Mash Tun
Sensor Assembly
Needle valve
Element
Sensor Assembly
Brew Kettle
Stage 4: Boil
Input 1
Valve 1
Valve 2
Valve 3
At the beginning of the boil stage valve 2 change outputs and valve 3 will close to isolate the mash tun
The pump and element are then switched on and the wort is heated up to 100°C
Once boiling begins it will continue for as long as the user defined recipe dictates. Prompts will be delivered to the users smart phone when hop and adjunct additions are required.
Near the beginning of the boil the user will be prompted to disconnect their mash tun and connect an external chiller in its place (if owned)
Near the end of the boil, valves 2 and 3 will open allowing boiling wort to be passed through the immersion chiller to sanitise it.

## Slide 5
Pump
Sparge Tank or tap connection
Sensor Assembly
Needle valve
Element
Sensor Assembly
Brew Kettle
Stage 5: Cooling
Input 1
Valve 1
Valve 2
Valve 3
For safety purposes the user will be prompted to confirm correct fitment of a cooler before proceeding to the cooling stage. If any option other than passive cooling is selected then the pump will then run to recirculate the wort. The system will then attempt to bring the wort to a user defined temperature, notifying the user once this occurs.
Multiple options exist for cooling the wort depending on the users equipment and preference. The wort can be cooled by connecting an external cooler (Immersion *shown above*, counterflow or plate chillers) in place of the mash tun, internally by a counterflow chiller or transferred hot to the fermenter and cooled passively.
If this temperature is unable to be reached e.g. the cooling water used is at a higher temperature than the target cooling temperature. Then the user will be notified that the cooling process has stalled. They can either select to finish the process there, or adjust the temperature of the cooling water and continue the process.

## Slide 6
Pump
Sparge Tank or tap connection
Sensor Assembly
Needle valve
Element
Sensor Assembly
Brew Kettle
Stage 6: Transfer
Input 1
Valve 1
Valve 2
Output 1
After the cooling phase is complete the pump will turn off. The user will be prompted to ensure output 1 is not below the surface of the wort in the brew kettle. This will allow air to be drawn into the lines and the wort to be drained back into the kettle. (This will drain any wort that is higher than the wort level in the kettle)
Valve 3
Valve 2 will then change outputs and valve 3 will close with the remaining wort draining back into the kettle.
At this stage the user can either select a pumped transfer to their fermenter (Kettle Output – Output 1) *shown above* or a manual transfer (valve 1 allows direct pass trough from Kettle Output – Input 1) if the user doesn’t want wort remaining in the lines.
Kettle Output
Fermenter

## Slide 7
Pump
Sparge Tank or tap connection
Mash Tun
Sensor Assembly
Needle valve
Element
Sensor Assembly
Brew Kettle
Stage 7: Cleaning
Fill system with water by connecting Input 1 to a household tap
Input 1
Valve 1 will then open allowing x amount of water into the Brew Kettle
Valve 1
Valve 2
Valve 3
Valve 1 will then change inputs and the pump and heater will turn on, pumping hot water throughout the system for a user defined time period
Valves 2 and 3 will also open to allow sanitisation of the mash tun
The waste water is then pumped out of the system and cleaning is complete